## Slide 1: Ca doj encryption bulletin round table discussion
Karl Grover, City of Roseville
Northern california apco chapter meeting
11/12/2020

## Slide 2: agenda
What’s the Bulletin and Why is it Important?
What is Encryption?
How Can My Agency Comply?
When Does My Agency Need to Respond?
Resources
Round Table Discussion

## Slide 3: What’s the bulletin and why is it important?
CalDOJ Bulletin #20-09-CJIS released 10/12/2020
FBI and CalDOJ require radio transmission of CJI and PII to be encrypted
  Criminal Justice Information- criminal history i.e. arrest records, wanted persons, etc.
    Restricted vs. Unrestricted categories in CJIS Security Policy
  Personally Identifiable Information- name, SSN, passport #, military ID, ID #, DL, etc.
Ensures protection of sensitive data as defined in FBI and CLETS policies, practices and procedures

## Slide 4: What is encryption?
Encryption is a method of scrambling data so that ONLY authorized parties can RX
Encrypted and “clear” communications typically have the same coverage and clarity
Encrypted transmissions can only be decrypted by radios that are capable of, provisioned, AND programmed to do so
  WARNING: encrypting ALL transmissions decreases transparency and increases interoperability challenges with other agencies plus may face additional challenges (i.e. failed AB-1555)
Different algorithms (i.e. ADP, DES, AES) and key bit sizes (i.e. 40, 128, 256)
  Federal standard = AES 256-bit
Encryption best practices – plan, standards, program, train, test, key mgmt., outreach

## Slide 5: How can my agency comply?
To comply with FBI and DOJ requirements, there are 2 options:
  1- Encrypt radio traffic with acceptable standards
    Provides the ability to securely broadcast all CJI and all combinations of PII
    128-bit or higher per CJIS Security Policy
  2- Change agency policy to restrict radio transmission of certain CJI & PII
    Use the radio except when sending restricted CJI and some combinations of PII
      Alternative acceptable methods include MDC’s and cell phones

## Slide 6: When does my agency Need to respond?
If your agency is not currently in compliance, then an Implementation Plan must be sent to Cal DOJ by 12/31/2020
  Note: DOJ understands this can have significant operational, technical and/or financial impacts so it should be restated DOJ expects a plan not a solution by 12/31/2020
The implementation plan should include:
  Agency letter head signed by the Agency Head (i.e. Chief, Sheriff)
  Detailed description of how:
    communications will be brought into compliance; or;
    how the risks will be mitigated via policy change
  Estimated timeline to implement encryption or policy change in order to achieve compliance

## Slide 7: resources
CalDOJ bulletin link:
https://oag.ca.gov/sites/all/files/agweb/pdfs/info_bulletins/20-09-cjis.pdf
CalDOJ contact info:
  Different agencies have different DOJ reps depending on geographic area
    Contact your agency’s representative via DOJ’s CLEW (CA Law Enforcement Web, http://clew.doj.ca.gov/)
  Or, email the CLETS Administration Section @ CAS@doj.ca.gov or call (916) 210-4240
FBI CJIS Security Policy (i.e. 5.10.1.2 Encryption, page #64)
https://www.fbi.gov/services/cjis/cjis-security-policy-resource-center
AB-1555: failed, but would require encrypted audio to be provided & released to requestors
https://leginfo.legislature.ca.gov/faces/billTextClient.xhtml?bill_id=201920200AB1555
DHS Cyber & Infrastructure Security Agency – Encryption best practices
https://www.cisa.gov/publication/encryption

## Slide 8: Round table discussion
Q & A
Discussion